## Slide 1: Maths 3C
2D Rigid Analysis in C++
Ben North Bharat Kunwar Saleema Hughes Sarah Lemasney Stephen Milonas

## Slide 2: Stages
INPUT NODES, MEMBERS, FORCES, SUPPORTS
CALCULATE THE DEGREES OF FREEDOM
FORMULATE THE GLOBAL STIFFNESS MATRIX AND MATRIX INVERSION
IMAGE PRODUCED ON AUTOCAD SHOWING THE PREDICTED DEFLECTION
WORK OUT THE DEFLECTIONS AND ROTATIONS

## Slide 3
Data Input
The first line is the number of nodes minus 1 (first node is 0)
NODES
n
0 0.1 0.2
1 1.2 1.4
The first column represents the node ID
The second column represents the x co-ordinate
The third column is the y co-ordinate

## Slide 4: Data Input (continued)
n
0 0 1 1 1 1
Last member ID
Current ID member
MEMBERS
End 0
End 1
E, A and I values respectively

## Slide 5: Data Input (continued)
LOADS
SUPPORTS
1 1 -1
-1
End of loads input
0 0 0 1
0 2
-1
End of support input
Node number
Magnitude of the force
Direction in the y axis
Node number
0= fixed in x direction
1= fixed in y direction
2= rotational fixity
Direction

## Slide 6: Degrees of Freedom
Member | 0 | 1 | 2 | 3
X | 0 x 3 = 0 | 1 x 3 = 3 | 2 x 3 = 6 | 3 x 3 = 9
Y | (0 x 3) + 1 = 1 | (1 x 3) + 1 = 4 | (2 x 3) + 1 = 7 | (3 x 3) + 1 = 10
ϴ | (0 x 3) + 2 = 2 | (1 x 3) + 2 = 5 | (2 x 3) + 2 = 8 | (3 x 3) + 3 = 11
(a x b) + c = d
where:
a = Member ID
b = Degrees of freedom at one node
c = +0 for x-axis, +1 for y-axis, +2 for rotational
d = Degrees of freedom of the system

## Slide 7: Forces
Fx1
Fy1
Fy2
Fx2
Fx1 = (-)F Cosθ = (-)F Lx/L
Fx2 = F Cosθ = F Lx/L
Fy1 = (-)F Sinθ = (-)F Ly/L
Fy2 = F Sinθ = F Ly/L
x
y
Lx = x2 – x1
Ly = y2 – y1

## Slide 8: Moments
M1 = EI/L(4θ1+2θ2+6d/L)
M2 = EI/L(2θ1+4θ2+6d/L)
x
y
Lx = x2 – x1
Ly = y2 – y1
M1
M2

## Slide 9
Account for supports
If node 1 is fixed in the y axis, the following would be introduced...

## Slide 10
Account for supports (continued)
1
0
0
0
0
0
0
0
0
0
0

## Slide 11: Global Stiffness Matrix

## Slide 12: EA/L - 12EI/L3
Loop ThisAxis from 0 to 1 {
Loop ThatAxis from 0 to 1 {
MemberStiffness = EA/L - 12EI/L3 for ThisAxis and ThatAxis
Loop ThisQuadrant from 0 to 1 {
Loop ThatQuadrant from 0 to 1 {
Determine This and That position in the global stiffness matrix
If leading diagonal, add to the global stiffness matrix
Else, subtract from the global stiffness matrix
}
}
}
}

## Slide 13
θ1
Δ
θ2
e
e = elongation
Δ = displacement
θ1, θ2 = rotation at each end
Deflection, rotation, forces and moments

## Slide 14
T = tension
F = shear force
M1, M2 = moments at each end
T = e(EA/L)
F = Δ(12EI/L3) + θ1(6EI/L2) + θ2(6EI/L2)
M1 = Δ(6EI/L2) + θ1(4EI/L) + θ2(2EI/L)
M2 = Δ(6EI/L2) + θ1(2EI/L) + θ2(4EI/L)
Deflection, rotation, forces and moments

## Slide 15: Output
Stiffness.txt Log of how the stiffnesses are compiles
Data.txt Forces, moment and deflections and rotations for each member
Drawing.dwg This is the file that contains the AutoCAD drawing

## Slide 16: Program Demonstration!

## Slide 17: Any questions??

## Slide 18: Thanks!
Hope that made sense =]